## Slide 1: X Plane Virtual Traffic Scratchpad
20200712/bm98

## Slide 2
S-ID REG T E-ID REG T D HL BAS TOP Segs
DEF K2 3 KLMNO K2 11 F 2 180 450 J13-J14-J15
LAT LON IDENT APT REG Type
46.646819444 -123.722388889 AAYRR KSEA K1 4530263
C LAT LON ELE FRQ CLS VAR IDENT APT REG NAME+SUFFIX
12 47.434333333 -122.306300000 369 11030 25 0.000 ISNQ KSEA K1 SEATTLE-TACOMA INTL DME-ILS
S-ID REG LAT LON E-ID REG LAT LON HL BAS TOP (Mid)LAT LON
DEF-K2 KLMNO-K2 2 180 450

## Slide 3
Acft Loc:
Lat / Lon / Alt
GenRange:
100 nm
ReGen:
1/4 Range
IFR enroutes
High
IFR enroutes
Low
VFR
artificial
Virt Acfts
Loc: Lat / Lon / Alt
HDG: degm
TAS: kts
Route: ID
Gen Pool
Update Pool
Send
Pool
Check
Pool
Out of range

## Slide 4
Acft Para:
Trk / VS / TAS
Acft Loc:
Lat / Lon / Alt
Acft ID:
Hex / CallSign / Reg
Type
From / To
1 StdTurnRate = 3° per second turn
| turn angle @const speed = 3°/sec
| radius of turn @const speed
| step distance @const speed
Dist
r
c
Linear Approx Test for dt = 1 sec:
Dist@100kt ~51m / => r=983m -> c~ 51m
Circles
Virtual Traffic VFR Aircraft Model

## Slide 5
Virtual Traffic VFR Aircraft Model
Commands
A=AcftType;[runway_ID] # an acft type and an optional runway id
S=knots # new TAS [kt] starting at next segment (default 100kt)
D=dist # a straight segment [nm]
T=[+-]angle # a turn segment [°] (abs <=360)
V=[+-]vs;agl # ascent or descent @vs starting at next segment (def 0ft/Min)
Create aircraft
Conditions
Segments
A=PC6T; LSZH_RW14 # a new PC6, starting at LSZH RWY14
S=95 # init at 95 kts
V=1000;500 # for the next segment climb to 500agl@1000ft/min
D=2 # straight for 2nm
T=180 # right turn of 180°
V=800;1000 # for the next segment climb to 1000agl@800ft/min
D=10 # straight for 10 nm
S=120 # speed up ; note this is instantaneous (simple model)
V=500;3000 # for the next segment climb to 3000agl@500ft/min
T=-30 # left turn of 30°
D=5 # straight for 5 nm
H=225 # now turn to HDG 225°
D=100 # straight for another 100 nm – just let it fly..
… once the acft reaches the end of the last segment it will be removed
H=hdg # new heading [°] (<=360)
Example Script
VFR Aircrafts are created from random scripts at random airports within
the observed range, at the start of a random runway using the rwy heading
The initial altitude (ground level) is given by the runway elevation.
V= command accepts a positive relative altitude (agl) where the reference is the runway elevation (can still hit rocks though)
Turns are relative to the current track, and start with the rwy heading
H= command goes to an absolute heading

## Slide 6
A=PC6T;LSZH_RW14 # a new PC6
S=95 # init at 95 kts
V=1000;1000
D=3
T=180
V=800;1500
D=6
T=120
S=140 # speed up
D=6
V=500;2000
D=6
T=120
V=500;3000
D=18
T=60
D=6
T=180
V=-800;2200
D=6
T=-60
V=300;3000
D=26
T=-150
V=-400;2800
D=100
180°
300°
60°
0°
120°
300°
240°
90°
1000@1000
3000@500
180°
2200@-800
3000@300
1500@800
2000@500
2800@-400
3nm
6nm
6nm
6nm
140kt
95kt
18nm
6nm
6nm
26nm
100nm

## Slide 7
A=C172;LSZH_RW14
S=95 # init at 95 kts
V=500;1000
D=2
T=180
D=4
T=180
S=60
V=400;0
D=2
S=1
D=1
180°
0°
1000@500
2nm
4nm
95kt
180°
2nm
000@400
60kt
1kt
1nm

## Slide 8
A=C172;LSZH_RW14
S=95 # init at 95 kts
V=500;1000
D=2
T=180
D=4
T=180
S=60
V=400;0
D=2
S=1
D=1
360°
0°
500ft@200
3nm
2nm
90kt
180°
2nm
000ft@400
60kt
10kt
1nm
120°
120°
90°
90°
90°
1.5nm
1.5nm
2000ft@1000
120kt
2000ft
1000ft
2000ft@1000
100ft@1000
1000ft@500
95kt
1000ft
2.5nm
1nm
1nm
3nm
1.5nm